## Slide 1: Cajalco Road Concrete Gravity Dam
2021 Senior Design Presentation
Group 2
May 6th, 2021
Notes: Speaker:

## Slide 2: Outline
Project Introduction/Statement
Dam Design
Spillway
Outlet Works
Pipeline
Pumps
Water Tank
Roadway
Environmental, Sustainability, and Constructability
Cost Estimate
Summary
Notes: Speaker: Jonathan

## Slide 3
Introduction
Cajalco Creek, CA
Water
  Demand:
    1.8 million gallons/day
    54.75 million gallons/month
  Purchase from Metropolitan:
    0.984 million gallons/day
    29.92 million gallons/month
  Dam Capacity:
    157.67 million gallons
Type of Dam
  Concrete Gravity

## Slide 4
Project Statement
Concrete Dam
Inclined Intake Tower
Road 1
Road 2
Eagle Canyon Road
Water Tanks
Pipeline
Hammer Head Turn out
N

## Slide 5: Outline
Project Introduction/Statement
Dam Design
Spillway
Outlet Works
Pipeline
Pumps
Water Tank
Roadway
Environmental, Sustainability, and Constructability
Cost Estimate
Summary
Notes: Speaker: Jonathan

## Slide 6
Dam Design: Concrete Gravity Dam
Characteristics:
Solid mass concrete
Self Weight used to resist forces
Integrated Spillway
Rock Foundation Recommended
Notes: Pine Flat Dam (Fresno, CA) in image

## Slide 7
Dam Design: Location
Eagle Canyon Rd.
Cajalco Rd.
15 Frwy
Site Location
Lake Mathews
N
  Geotechnical Reports in project location:
    States top layer (10’) composed of Clay soil
    Bottom Layer composed of 90% Granite

## Slide 8
Dam Design: Seismicity
Seismic Analysis:
  Faults in Proximity:
    Elsinore
    San Andreas
    San Jacinto
    Sierra Madre
Peak Ground Acceleration:
  PGA (Horizontal) = 0.834 g
  PGA (Vertical) = 0.556 g

## Slide 9
Dam Design: Water Capacity
Determination of Water Capacity
  (Ripple Method)
  483.84 acre-ft
  Water Level at 56 ft
157.7 Million
Gal. Difference

## Slide 10
Dam Design: Dimensions
Concrete Gravity Dam:
Slope = 1:1
10’
56’
16’
Water
Reservoir
Shear Key
Upstream
Downstream

## Slide 11
Dam Design: Structural Analysis
+
FR,water
Hydrostatic Pressure:
FR,pp
Passive Pressure:
FR,UL
Uplift Pressure:
Fweight
Fhor., seismic
Fver., seismic
Ffriction
Notes: Put labels inside picture, get rid of numbering

## Slide 12
Dam Design: Structural Analysis
FR,pp=340 kip/ft
Fweight
Ffriction = 172 kip/ft
Fsiesmic,hor. = 316 kip/ft
Sliding Check
Sliding Check w/ Seismic
+
Factor of Safety: 5.24 > Allowable FOS = 1.5
+
Factor of Safety : 1.51 > Allowable FOS = 1.1
FR,water= 97kip/ft
FR,water= 97kip/ft
FR,pp=340 kip/ft
Ffriction = 172 kip/ft
Fweight

## Slide 13
Dam Design: Structural Analysis
Overturning Check
Overturning Check w/ Seismic
MPP = 6,810 k-ft
+
+
Mwater = -2,739 k-ft
Mweight = 23,534 k-ft
MUL = -7,722 k-ft
Factor of Safety: 1.11 > Allowable FOS = 1.1
Mhor., seismic =
-8,605 k-ft
Mver., seismic =
-10,094 k-ft
MPP = 6,810 k-ft
MUL = -7,722 k-ft
Mweight =
23,534 k-ft
Factor of Safety: 2.90 > Allowable FOS = 1.5
Mwater =
-2,739 k-ft
Notes:     Add force values to images, split factor of safety, different cases

## Slide 14
Dam Design: Structural Analysis
Shear Check:
ACI 318-14
øVn (kip)
20,671
Hydrostatic Pressure:
Vu (kip)
581
>
Notes:   Don’t go into the numbers just say concrete strength is adequate to resist shear loading

## Slide 15
Shear Key Design
Fact. pressure
Ultimate Moment: (Assume 1’ deep Cross Section)
Mu = 1.6(P*Y) = 3225.6 kip-ft
Shear Key Reinforcements:
Concrete Cover of 3” (ACI Table 20.6.1.3.1)
As = 5.82 in^2 (per foot)
(Bundle two bars per section)
Spacing = 6” OC
Use:
2#11 bars @ 6” OC
Min Steel #5 bars @ 12” OC (Transverse Direction)
Transverse
Longitudinal

## Slide 16: Outline
Project Introduction/Statement
Dam Design
Spillway
Outlet Works
Pipeline
Pumps
Water Tank
Roadway
Environmental, Sustainability, and Constructability
Cost Estimate
Summary
Omar Abdelhadi
Notes: Speaker: Jonathan

## Slide 17
Spillway
Spillway allows controlled discharge of excess water from reservoir
Cajalco Creek is a tributary of Temescal Wash
Peak discharge in Cajalco Creek determined to be 3,070 cfs
Omar Abdelhadi
Cajalco
Creek
Temescal
Wash
Project
Site

## Slide 18
Spillway - Crest
Omar Abdelhadi
Trapezoidal crest allows vehicles to traverse entire structure
Wider crest requires less hydraulic head to reach target flowrate
100 ft
16°
Slope
Reservoir

## Slide 19
Spillway - Channel
Narrowing the channel reduces width of stilling basin and subsequently construction costs
height of the channel walls with freeboard of 3 feet.
Omar Abdelhadi
142 ft
40 ft
Upstream
Downstream
At Narrowest Portion:

## Slide 20
Spillway – Stilling Basin
Hydraulic jump dissipates 68% of incoming water’s energy
Based on USBR Type II Stilling Basin
Omar Abdelhadi
Streambed

## Slide 21
Spillway – Structural Design
High water height causes large moment in spillway walls
Flexural reinforcement needed to achieve moment capacity
Omar Abdelhadi
#10 bar
#10 bars @ 10” on Center
Mu = 63.1 Kip-ft
Vu = 10.5 Kip

## Slide 22: Outline
Project Introduction/Statement
Dam Design
Spillway
Outlet Works
Pipeline
Pumps
Water Tank
Roadway
Environmental, Sustainability, and Constructability
Cost Estimate
Summary
Notes: Speaker: Jonathan

## Slide 23
281ft north of dam upstream
Water Supply Solution: Incline Intake Tower
What does it do?
How does one look?
Where is it located?

## Slide 24
Outlet Works: Hydraulics
Main Hydrological Features:
Drainage of the reservoir for emergency purposes
  Required by the Division of Safety of Dams
  50% drawdown (7-10 days) & 100% drawdown (20-30 days)
Drainage of the reservoir for operational purposes
  Delivering water to pump station with pipeline

## Slide 25
Outlet Works: Hydraulics
Emergency Release Criteria
Volumetric capacity of reservoir: 157.7 million gallons
50% Drawdown for 7 – 10 days |  | 
Time (days) | Discharge (gallons/day) | Discharge ()
7 | 11,261,419 | 17.42
10 | 7,882,993 | 12.20
100% Drawdown for 20 – 30 days |  | 
Time (days) | Discharge (gallons/day) | Discharge ()
20 | 3,941,497 | 6.10
30 | 2,627,664 | 4.07
50% Drawdown for 7 – 10 days |  | 
Time (days) | Discharge (gallons/day) | 
7 | 11,261,419 | 17.42
10 | 7,882,993 | 12.20
100% Drawdown for 20 – 30 days |  | 
Time (days) | Discharge (gallons/day) | 
20 | 3,941,497 | 6.10
30 | 2,627,664 | 4.07
Orifice Discharge Formula:

## Slide 26
Outlet Works: Hydraulics

## Slide 27
Minimum required static F.O.S: 1.5
Minimum required seismic F.O.S: 1.1
Assumptions: cohesionless soil, 120 pcf unit weight, 32o friction angle
Angle of inclination: 20 degrees
Actual factor of safety: 1.72
Outlet Works: Geotechnical

## Slide 28
Outlet Works: Structural
Structure:
Reinforced Concrete
Loads Considered: Dead Load, Seismic, & Hydrostatic.
Dimensions per ACI requirements
Total Length down slope: 268’
Dimensions of Shear Keys:
Depth: 5’
Thickness: 1’
Width: 10’
Spacing 13’: 17 shear keys
Shear Keys

## Slide 29
Outlet Works: Structural
Shear Key Reinforcement:
F(Seismic)
F(Hydro.)
As = 3.27 in^2 (2-piece bundle)
Concrete Cover of 3” (ACI Table 20.6.1.3.1)
Spacing = 6” OC
Use: 2#14 Bars @ 6in OC
(ASCE 7-10 Load Combo: 1.2(D+F) + 1.0E+1.6H)
W.L.

## Slide 30: Outline
Project Introduction/Statement
Dam Design
Spillway
Outlet Works
Pipeline
Pumps
Water Tank
Roadway
Environmental, Sustainability, and Constructability
Cost Estimate
Summary
Notes: Speaker: Jonathan

## Slide 31
Pipeline Design Introduction
Consists of 3,522 feet of ductile iron pipeline running from the inclined intake tower to the pump station and lastly, to the tanks
The pipeline will lay 3 feet below our roadway
Designed our pipeline to fit the demand of 1.8 million gallons throughout a 9-hour period
Water Tanks
Pump Station
Inclined Intake Tower

## Slide 32
Pipeline Diameter
Demand Flow Rate: 14.85 cfs

## Slide 33: Pipe Trench
Trench will be dug along path of the pipe.
Embedment of 1 ft on each side for structural support.
Cover of 3 ft soil for deflection purposes.
Pipe 1: 36” interior diam
Pipe 2: 18” interior diameter.
Length = 267 ft.
Length = 3255 ft.

## Slide 34: Pipe: Thickness and Deflection
Thickness
Depends on:
  Interior existing pressures: 288 psi
  Strength of materials: ductile iron / cement mortar lining
  Required thickness: 0.15 in.
  Actual thickness: 0.30 in.
  Total pipe 1 diameter: 37.5 in.
  Total pipe 2 diameter: 19.5 in.
Deflection
Depends on:
  Dead and live loads
  Strength of materials
  Embedment dimensions
  Allowable Deflection: 0.75 in.
  Pipe 1 deflection: 0.35
  Pipe 2 deflection: 0.09 in.

## Slide 35: Pipe Thrust
  Thrust force
    45-degree bends: 66 kips.
    90-degree bends: 122 kips.
  Welds where pipe diameters and wall thicknesses are equal.
  Flanges where pipe diameters are different.
  Required restrained length
      75 ft for 45-degree angles
      180 ft. for 90-degree angles
  Areas of thrust blocks
      33 ft^2
      60 ft^2

## Slide 36: Pipeline Final Recommendations
Length of Pipeline: 3522 ft
Nominal diameter of the pipe: 19.5 inches
Interior Diameter of the pipe: 18 inches
Pipeline Material: Ductile Iron
  Cement Mortar Lining
  Wall Thickness of pipe: 0.3 inches
N
Inclined Intake Tower
Pump Station
Concrete Dam
Pipeline
Water Tanks
Eagle Canyon Road

## Slide 37: Outline
Project Introduction/Statement
Dam Design
Spillway
Outlet Works
Pipeline
Pumps
Water Tank
Roadway
Environmental, Sustainability, and Constructability
Cost Estimate
Summary
Notes: Speaker: Jonathan

## Slide 38
Pumps

## Slide 39
Determining Pump Head
Discharge Flow Rate: 14.85 cfs
Main pipeline diameter: 18 in
Velocity within pipeline: 8.4 ft/s
Bernoulli’s Energy Equation
+
Pump Head = 332 ft

## Slide 40
Pump Recommendations
Recommended Design Criteria
  Centrifugal Pump
  Overcome head of 332 feet
  Minimum Efficiency of 80 %
  Output Power of 280 HP
  9 - hour period

## Slide 41
Pump Station
Location:
  Connected to the Dam
  33 feet to the Right of the Spillway
Material:
  Concrete
8 ft
8 ft
18 ft
Front View
18 ft
28.62 ft
Side View
Top View
Dimensions:
Pump House

## Slide 42: Outline
Project Introduction/Statement
Dam Design
Spillway
Outlet Works
Pipeline
Pumps
Water Tank
Roadway
Environmental, Sustainability, and Constructability
Cost Estimate
Summary
Notes: Speaker: Jonathan

## Slide 43
Introduction of the Water Tanks Location ​
N
Water tank is located North of the concrete gravity dam
The elevation of the concrete gravity dam is at 830 ft
The elevation of the water tank is 1,062 ft.
Elevation difference of 232 ft.
Concrete Dam
Pipeline
Water Tanks
Road 1
Road 2
Eagle Canyon Road

## Slide 44
Purpose of Water Tanks
Mining conglomerates
  1.8 million gallons of water
  Minimum water tank capacity of 450,000 gallons
Fire department
  3.15 million gallons
Total water tank size capacity
  3.6 million gallons

## Slide 45
Water Tank Sizing
 | Table 2 Additional Water Requirement | 
Design Size [Gal] | Riverside Fire department Requirement [Gal] | Total [Gal}
450,000 | 3150000 | 3,600,000
Daily Volume = 225,000 gal
Fire Department Volume = 1,575,000
Free Board Height
30ft
4ft
Fire Department Volume = 1,575,000
Daily Volume = 225,000 gal
Radius = 50 ft
Chart: Water Demand
| 6:00am | 7:00am | 8:00am | 9:00am | 10:00am | 11:00am | 12:00am | 1:00pm | 2:00pm | 3:00pm | 4:00pm | 5:00pm
Water Demand | 150000 | 0 | 50000 | 100000 | 150000 | 200000 | 250000 | 300000 | 350000 | 400000 | 450000 | 300000
450,000

## Slide 46
Water Tank Structural Design
 | Maximum Stress | Allowable Stress [D-100] Table 5 & 3
Shear | 19,700 psi | 21,000 psi
= 100 ft
= 30 ft
0.375’’

## Slide 47
Water Tank Structural Design
Anchorage System | 
Concrete Strength | 3,500 psi
3/4 F1554 Gr.36 | # of bolts per tank [304]
SET 3G | Adhesive
100’0’
66’5’
5’0’
Foundation Volume = 649 ft^3
Slab Volume = 16,552 ft^3
66’5’

## Slide 48
Excavation of Water Tanks Location
Total Excavation Volume: 7532 cubic yds
Highest initial elevation is around 1068 ft
Ground will be flattened to an elevation of 1058 ft
Figure A
Figure B
Figure C
A
A'
B
B'
Notes: Finally I will be talking about the excavation of the water tanks location. Due to the uneven slope of the location an excavation of 7532 cubic yds will be required to flatten the area to an elevation of 1,068ft.

## Slide 49: Outline
Project Introduction/Statement
Dam Design
Spillway
Outlet Works
Pipeline
Pumps
Water Tank
Roadway
Environmental, Sustainability, and Constructability
Cost Estimate
Summary
Notes: Speaker: Jonathan

## Slide 50
Roadway Introduction
Concrete Dam
Water Tanks
Road 1
Road 2
N
Inclined Intake Tower

## Slide 51
Roadway Overview
Concrete Dam
Inclined Intake Tower
Road 1
Road 2
Eagle Canyon Road
Water Tanks
Pipeline
Hammer Head Turn out
N

## Slide 52
Hammer-Head Turnaround
96’
16’
Location: East end of dam
  Allows for 3pt turn
  ~37% smaller by area than a cul-de-sac (r=28’)
  Designed for utility trucks
    Accommodates vehicles up to 24’ in length

## Slide 53
Road 1 – Dam Road
N
Eagle Canyon Road
Concrete Dam
Turnout
Turnout
+ Intake Tower Entrance
0+00 (#0)
7+50 (#30)
Total Length: 750 ft
Average Grade: 15%
Inclined Intake Tower
Elevation: 897 ft
Elevation: 1009 ft
Hammer-Head Turnout
Road 1
7+50 (#30)
Elevation: 1009 ft
Notes: >> show where hammer head turnout is from Paul's slide
>> Road 1 introduction
>Road from our concrete dam to Eagle canyon road.
>Total length of 750 ft
> Average grade of 15 %
>starts at elevation:897 ft
>ends at elevation: 1009 ft
>> Intake tower
>as previously mentioned in the Intake tower access road section of this presentation
both the intake tower and the dam share this access road and is connected by a turnout
as shown in the topographical map.
>>Turnout
> there is another turnout more south closer to the dam
> with this many turouts, drivers should have no problem finding a place to turn their vehicle around
or park on this road.

## Slide 54
Road 1 – Dam Road
N
Eagle Canyon Road
Concrete Dam
Turnout
Turnout
+ Intake Tower Entrance
0+00 (#0)
7+50 (#30)
Total Length: 750 ft
Average Grade: 15%
Inclined Intake Tower
Elevation: 897 ft
Elevation: 1009 ft
Hammer-Head Turnout
Road 1
7+50 (#30)
Elevation: 1009 ft
Notes: >> show where hammer head turnout is from Paul's slide
>> Road 1 introduction
>Road from our concrete dam to Eagle canyon road.
>Total length of 750 ft
> Average grade of 15 %
>starts at elevation:897 ft
>ends at elevation: 1009 ft
>> Intake tower
>as previously mentioned in the Intake tower access road section of this presentation
both the intake tower and the dam share this access road and is connected by a turnout
as shown in the topographical map.
>>Turnout
> there is another turnout more south closer to the dam
> with this many turouts, drivers should have no problem finding a place to turn their vehicle around
or park on this road.

## Slide 55
Intake Tower Turnout/ Entrance
Inclined Intake Tower
Road 1
Eagle Canyon Road
Eagle Canyon Road
Hammer Head Turnout
Pump Station
Pipeline
N
Concrete Dam
0+00 (#0)
Elevation: 897 ft
7+50 (#30)
Elevation: 1009 ft
Intake Tower
Turnout/ Entrance
Notes: >> Intake tower
>our access road to the intake tower is the same
road we are using for our access road to the dam.
>we decided to use a turnout to connect the intake tower to our
access road since it was relatively close to our access dam road
which we designed first
>More details on the access road will be provided later in the Roadway section
of this presentation.

## Slide 56
Road 1 – Dam Road
N
Eagle Canyon Road
Concrete Dam
Turnout
Turnout
+ Intake Tower Entrance
0+00 (#0)
7+50 (#30)
Total Length: 750 ft
Average Grade: 15%
Inclined Intake Tower
Elevation: 897 ft
Elevation: 1009 ft
Hammer-Head Turnout
Road 1
7+50 (#30)
Elevation: 1009 ft
Notes: >> show where hammer head turnout is from Paul's slide
>> Road 1 introduction
>Road from our concrete dam to Eagle canyon road.
>Total length of 750 ft
> Average grade of 15 %
>starts at elevation:897 ft
>ends at elevation: 1009 ft
>> Intake tower
>as previously mentioned in the Intake tower access road section of this presentation
both the intake tower and the dam share this access road and is connected by a turnout
as shown in the topographical map.
>>Turnout
> there is another turnout more south closer to the dam
> with this many turouts, drivers should have no problem finding a place to turn their vehicle around
or park on this road.

## Slide 57
Retaining Wall
Inclined Intake Tower
Road 1
Eagle Canyon Road
Hammer-Head Turnout
Pump Station
Intake Tower
Turnout/ Entrance
N
Concrete Dam
Turnout
0+00 (#0)
Elevation: 897 ft
7+00 (#28)
Elevation: 1000 ft
Retaining Wall
Average Grade: 15%
Total Length: 700 ft
Notes: >> show where hammer head turnout is from Paul's slide
>> Road 1 introduction
>Road from our concrete dam to Eagle canyon road.
>Total length of 750 ft
> Average grade of 15 %
>starts at elevation:897 ft
>ends at elevation: 1009 ft
>> Intake tower
>as previously mentioned in the Intake tower access road section of this presentation
both the intake tower and the dam share this access road and is connected by a turnout
as shown in the topographical map.
>>Turnout
> there is another turnout more south closer to the dam
> with this many turouts, drivers should have no problem finding a place to turn their vehicle around
or park on this road.

## Slide 58
Road & Retaining Wall Cross-Section

## Slide 59
Road & Retaining Wall Cross-Section

## Slide 60
Road & Retaining Wall Cross-Section

## Slide 61
Road & Retaining Wall Cross-Section

## Slide 62
Road 1
Cut/Fill Volume | 
Cut | 2,215 cubic yards
Fill | 3,837 cubic yards
Ratio: | 0.57
Average Grade: 15%
Station # | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
Stationing | 0+00 | 0+25 | 0+50 | 0+75 | 1+00 | 1+25 | 1+50 | 1+75 | 2+00 | 2+25 | 2+50 | 2+75 | 3+00 | 3+25 | 3+50 | 3+75 | 4+00 | 4+25 | 4+50 | 4+75 | 5+00 | 5+25 | 5+50 | 5+75 | 6+00 | 6+25 | 6+50 | 6+75 | 7+00 | 7+25 | 7+50

## Slide 63
Road 2 – Tank Road
Eagle Canyon Road
Water Tanks
N
Turnout
0+00 (#0)
Elev. 1026 ft
4+50 (#18)
Elev. 1063 ft
Total Length: 450 ft
Turnout: 2,400 sq. ft.
Average Grade: 8%

## Slide 64
Road 2
Cut/Fill Volume | 
Cut | 921 cubic yards
Fill | 4,210 cubic yards
Ratio: | 0.22
Average Grade: 8%
Station # | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
Stationing | 0+00 | 0+25 | 0+50 | 0+75 | 1+00 | 1+25 | 1+50 | 1+75 | 2+00 | 2+25 | 2+50 | 2+75 | 3+00 | 3+25 | 3+50 | 3+75 | 4+00 | 4+25 | 4+50

## Slide 65
Roadway Summary
Each roadway is created with design constraints and specifications in mind:
  Maximum grade of 16%
  Average End Method
  Single-lane roads, 2 ft shoulder, minimum of 1 turnout
 | Road 1 | Road 2 | Retaining Wall | Hammer-Head | Total
Total Length | 750 ft | 400 ft | 700 ft | 96 ft | 1946 ft
Average Grade | 15% | 10% | 15% | - | -
Cut | 2,215 cubic yards | 921 cubic yards | 1,633 cubic yards | 38 cubic yards | 6,429 cubic yards
Fill | 3,837 cubic yards | 4,210 cubic yards | 726 cubic yards | 75 cubic yards | 7,226 cubic yards
Number of Turnouts | 2 | 1 | - | 1 | 4
Drainage is expected to occur naturally along the slope of the roads.

## Slide 66
Roadway Summary
Each roadway is created with design constraints and specifications in mind:
  Maximum grade of 16%
  Average End Method
  Single-lane roads, 2 ft shoulder, minimum of 1 turnout
 | Road 1 | Road 2 | Retaining Wall | Hammer-Head | Total
Total Length | 750 ft | 400 ft | 700 ft | 96 ft | 1946 ft
Average Grade | 15% | 10% | 15% | - | -
Cut | 2,215 cubic yards | 921 cubic yards | 1,633 cubic yards | 38 cubic yards | 6,429 cubic yards
Fill | 3,837 cubic yards | 4,210 cubic yards | 726 cubic yards | 75 cubic yards | 7,226 cubic yards
Number of Turnouts | 2 | 1 | - | 1 | 4
Drainage is expected to occur naturally along the slope of the roads.

## Slide 67: Outline
Project Introduction/Statement
Dam Design
Spillway
Outlet Works
Pipeline
Pumps
Water Tank
Roadway
Environmental, Sustainability, and Constructability
Cost Estimate
Summary
Notes: Speaker: Jonathan

## Slide 68
Environmental – CEQA Checklist
Environmental Factors Potentially Affected:

## Slide 69
Environmental – Construction Mitigation, Emergency Planning, and Federal Regulations.
Sample: www.tinyurl.com/group2EAPsample

## Slide 70: Sustainability- Life Cycle Assessment
  Cement
  Sand
  Aggregate
  Fly Ash
  Rock
    Diesel
    Gasoline
Hauling Materials
    Distance
    Load of the vehicle + Material
    Gasoline
Material Production
Transportation of Construction Materials

## Slide 71: Sustainability- Life Cycle Assessment
  Excavation
  Mixing
  Pouring
  Curing
    Diesel
    Electricity
    Gasoline
Operation & Maintenance
  Road Repair
  Spillway Maintenance
  Dam Maintenance
    Diesel
    Gasoline
    Electricity
    Materials
Construction
            Use

## Slide 72
Sustainability- Climate Change/Adaptation
Sustainable Practices:
  Air Quality – reduce carbon emissions
  Recycle Material – reuse composite material
Adaptation Planning:
  Taking actions to reduce the negative impacts of climate change
  Climate Protection

## Slide 73
Sustainability- Other Future Risks

## Slide 74: Constructability
Constructability is the reflection of the design documents to ensure that the major issues are addressed early in the process.
1. Concrete batch plant
2. The materials need for the concrete plant
3. Transportation
4. The contractor lay out

## Slide 75: Constructability
5. Temporary Roadways
  All construction material will be delivered through a temporary roadways.
  A permit will be required when making these temporary roadways by the Riverside Building Department.
6. Constraints
  Avoid anything that will impact the local community and the wildlife in a negative way.
  Contractors are allowed to bring essential equipment to the site.
* All transportation will follow local and federal state requirements to avoid citations throughout the transportation as well as on the site.
N
N
Pathway to the work site from I-15

## Slide 76: Outline
Project Introduction/Statement
Dam Design
Spillway
Outlet Works
Pipeline
Pumps
Water Tank
Roadway
Environmental, Sustainability, and Constructability
Cost Estimate
Summary
Notes: Speaker: Jonathan

## Slide 77
Cost Estimate
Class 5: Order of Magnitude
Expected Accuracy Range: +30% to -50%
(AACE 18R-97)
Material/Work | Price ($)
Concrete | 32,325,094.91
Pipeline | 201,458.40
Water Tank | 3,000,000.00
Roadway | 465,909.24
Earthwork | 7,584,525.75
Pump Station | 3,000,000.00
Retaining Wall | 196000
Environmental (15%) | 7,015,948.24
Design (15%) | 7,015,948.24
Contingency (30%) | 14,031,896.49
Total Cost ($) | $ 74,836,781.27
Chart: Pie Distribution
| Concrete | Pipeline | Water Tank | Roadway | Earthwork | Pump Station | Retaining Wall | Enviormental | Design | Contingency
 | 32325094.9065 | 201458.4 | 3000000 | 465909.24 | 7584525.7488 | 3000000 | 196000 | 7015948.2443 | 7015948.2443 | 14031896.4886

## Slide 78: Outline
Project Introduction/Statement
Dam Design
Spillway
Outlet Works
Pipeline
Pumps
Water Tank
Roadway
Environmental, Sustainability, and Constructability
Cost Estimate
Summary
Notes: Speaker: Jonathan

## Slide 79
Summary
Project Objective
Design
  Dam
  Incline Intake Tower
  Pipeline
  Water Tanks
  Access Roads
  CEQA/Cost Estimate
Summary
Concrete Dam
Intake Tower
Water Tanks
Pipeline
Road 1
Road 2
N
Pump Station
Water Reservoir

## Slide 80
Questions?