## Slide 1: Turbo Trike Expo
Team 35-1/ TEAM 35-2
Advisor: Dr. Samuel Landsberger
SPONSOR: John Wieland, Inc. & Grid Alternatives, Inc.
Members: Loren Barton
Jihane Ait Bella
Hernan Reyes
Martin Morales
David Bonilla
Jairo Martinez
Wesley Aquino
Ivan Petean
Dillon Howard

## Slide 2: Project Organization
Turbo Tike Team
Advisor Prof. Samuel Landsbeger
Team 1 Lead/ Suspension
Loren Barton
Auto Braking
Martin Morales
Regenerative Braking/Safety
Dillon Howard
Team Sponsor John Wieland Inc & Grid Alternatives Inc
Team 2 Lead/ Steering
Jihane Ait Bella
Steering/Frame
Hernan Reyes
Solar Charging
David Bonilla
Suspension/Scale Modeling
Jairo Martinez
Roll Cage
Wesley Aquino
Roll Cage/Street Legal Design
Ivan Petean

## Slide 3: Agenda
Introduction
  Objectives and Constraints
  Global Impact
  Original Turbo Trike
Trike A and B
  Modifications
  Suspension
  Steering
  Roll Cage
Autobraking
Regenerative Braking
Solar Assist
Road Legal
Lateral Acceleration
Rollover Prevention
Scale Models
Jihane
David
Jihane
Dillon/ Loren
Wesley
Loren/ Jairo
Loren/ Jairo
Jihane/ Hernan
Wesley/ Ivan
Martin
Dillon
David
Ivan
Dillon
Dillon
Jairo/Loren/Hernan

## Slide 4: Project Schedule

## Slide 5: Objectives and constraints
Conceive, design and improve an electric three-wheeled vehicle for daily application.
Safe at speeds of 45 mph.
Improve power efficiency by implementing regenerative braking
Add solar panels to increase ideal range by 30 miles
Assuring safety of rider.
Accessibility for individuals up to 195cm

## Slide 6: Impact on the Planet
Majority of vehicles today use an internal Combustion Engine.
Contributes to air pollution and releasing CO2 into the atmosphere.
Benefit nature and fight against global warming.
Inefficient car
Aptera EV

## Slide 7: Original Turbo Trike
The Turbo Trike was constructed from a KMX Kolt Recumbent tricycle.
Kelly Controls KBL Series motor controller and 48V 3KW hub motor
2 lithium iron phosphate (LiFePo4) Batteries
Numerous ergonomic issues
Has shown to have stability issues and understeer when cornering.

## Slide 8: Original Turbo Trike

## Slide 9: Road Map
Turbo Trike Design Requirements
Model A
Model B
Simplicity
Roll Cage A
Driver Controls (Quick)
Comfort
Driver Controls (Precise)
Roll Cage A
Common Ground
Solar Panels
Auto Braking
Street Legal
Safe at 45 mph
Leaf Suspension
Go-Kart Steering
Long Roll Cage
Spring/Damper Suspension
Rack & Pinion Steering
Short Length Roll Cage
Solar Power
Outrigger Wheels
Lidar
Kelly Controller
Driver Pedals
Scale Models
Final Decision

## Slide 10: Model A

## Slide 11: Design Approach
Maximize Simplicity
Driver Protection
Improved Driver Controls
Minimal Modification to existing model
Minimize overall cost
Steering Wheel
Foot pedals
Visually appealing
Energy absorption zones on all sides
Safe for travel at 45 mph

## Slide 12: Suspension
Double Wishbone
Compressible Spoke
BMW Isetta Outboard Swing Arm

## Slide 13: Isetta Suspension

## Slide 14: Decision Matrix- Front Suspension
 | Minimal Space Occupied | Simplicity | Minimal Bump Steer | Total | Weighted Total
Weights | .3 | .5 | .2 | 1 | 
Compressible Spoke | 5 | 4 | 5 | 14 | 4.5
Double Wishbone | 1 | 2 | 3 | 6 | 1.9
Isetta Swing Arm | 4 | 1 | 5 | 11 | 2.7
Transverse Leaf | 3 | 3 | 3 | 9 | 3

## Slide 15: Leaf Suspension
The leaf suspension is sturdy and easy to fabricate
Minimal intrusion into driver area
Can be found on the Chevrolet Corvette
Leaf springs can be cheap and additional leaves may be added for greater loads

## Slide 16: Suspension Deflection
Trike weighs 2880N, or 293 kg with 96kg rider
COG lies 95cm along 150cm wheelbase
Half of the front weight is borne by each wheel, so 1000N at a front corner
Leaf curves, so shackle holes are below center point
Displacing 6.35 cm will flatten leaf, creating negative camber
F - Force
E - Young’s Modulus
b – Leaf Width
t – Leaf Thickness
𝛿 – Deflection
nm – Number of Master Leaves
ng – Number of Graduated Leaves
L – Leaf length

## Slide 17: Suspension
Leaf Displacement at Max Capacity
Very near the desired force for flattening

## Slide 18: Suspension
Leaf Strain Under Load
The leaf remains well within its elastic region under load
Additional leaves may still be added for additional force
Center plate screws may be moved to adjust ride height

## Slide 19: Role of the Steering System
The steering system, along with the suspension system allows the driver to easily and safely control the vehicle’s direction while driving.
Compared to the first generation steering system that had no suspension, we planned to implement a suspension system to our trike.
The steering system consists of a collection of components and linkages, which allows any vehicle (car, bicycle, motorcycle) to follow a desired path.
Most vehicle steering systems are composed of steering linkages, a steering column, a steering gear and a steering wheel.

## Slide 20: First Generation Steering System
The Turbo Trike Initially was designed with handlebars from side to side from driver.
Steering angles were limited and would range from 15-25 degrees depending on driver's body width.

## Slide 21: Objective: what Do we want to improve and why?
Reduce Tire scrub
(Apply Ackerman Steering principle)
Easier to steer
(incorporating a steering wheel)
comfort
(sitting and handling position)
Safety
(turning radius/roll over)

## Slide 22: History
The first automobile was invented more than 100 years ago.
The first automobiles were steered with a tiller.
In 1898, steering wheels were introduced as a standard feature in cars.
At the start, steering wheels had a simple design: consisted of wooden circles directly connected to the wheel axis.
They were extremely hard to turn, especially at low speeds.
In 1920, the first power steering system was invented to make the turn of the steering wheel easier.

## Slide 23: Different steering systems and geometries
Ackermann Geometry
Pitman Arm steering
Rack and Pinion Steering

## Slide 24: Ackermann Principle
Ackermann principle, is a common steering geometry that is used to reduce tire scrub when corning by making the inside wheel turn on a tighter radius than the outer wheel.
To achieve a smooth path the front wheel axis should intersect at an instantaneous center to the rear wheel axis, so that the front wheels create a concentric path.

## Slide 25: Decision Matrix- Steering
 | Simplicity | Weight | Cost | Weighted Total
Weights | 5 | 3 | 2 | 
Pitman arm | 20 | 10 | 9 | 39
Rack and pinion | 15 | 6 | 6 | 31

## Slide 26: Pitman Arm Steering
The Pitman arm moves the steering rack according to how you steer.
The steering rack is connected to the tie rods, which are connected to the steering arm.
The tie rods are the connection from the steering system to the wheels.

## Slide 27: Steering - Pitman Arm
Pitman arm with leaf spring suspension
Clamp shaft with screw stoppers and tie rod slot

## Slide 28: Turning Radius Calculations
Parameters ​ | 
Wheelbase(L)​​ | 1.48 m​
Track width(d)​​ | 1.22 ​m​
Inner Angle​(A) | 18.51°
Outer Wheel​(B) | 15.37°
Pitman Arm Steering with stopper
Assume
Turning Radius of 5 meters.
Actual Turning Radius
R= d/2+[L(cosec (A/2+B/2))] [Eq.1]
R= 5.69 meters
1.22 m
1.48 m

## Slide 29: Steering Ratio
Type of Vehicle | Steering Ratio
Normal Regular Cars | 12:1 to 20:1
Race cars | 10:1
Go-Kart | 1:1
Turbo Trike (Rack and Pinion steering) | 3:1
Turbo Trike (Pitman arm steering) | 1:1
Table- Steering ratio of different types of vehicles
Low Steering ratio = more effort to steer
High Steering ratio= less effort to steer
Steering ratio Equation
Steering ratio = (Steering wheel rotation angle)/(Steer angle at the tire wheel)

## Slide 30: Roll CAGE
Roll cage is designed to protect the passengers in the vehicle from:
  Roll Over
  Collision

## Slide 31: Roll Cage – Model A
Low Cost
Ease of Manufacturing and Assembly
Minimized joints while taking advantage of:
  Triangulation
  Diagonalization
Maximizing safety, while minimizing complex structures

## Slide 32: Triangulation
Basic tool for rigidity through shape
A diagonal member through connected corners protects a four-bar member from bending loads
  Placing structural members in pure tension/compression
Lightweight
  Use of less rigid materials won’t significantly affect the overall strength of the structure

## Slide 33: Benefits of Model A
Low seating position means low center of gravity
Minimal modifications require less time and money to perform
Lower weight increases range and efficiency
Simplicity of design allows for lower overall cost

## Slide 34: Material Property Analysis
Material | Ultimate Tensile Strength (MPa) | Elastic Modulus (GPa) | Yield Strength (MPa) | Fatigue Strength (Uncorrected) (MPa) | Shear Modulus (GPa)
AISI 1015 Steel (CDS) | 385 | 205 | 325 | 193 | 80
AISI 4130 Steel Annealed at 865 C | 560 | 190 | 460 | 280 | 80
6061-T6 | 241 | 74 | 145 | 121 | 26
2219-T87 | 379 | 73 | 393 | 190 | 27
7075-T6 | 572 | 72 | 434 | 286 | 27

## Slide 35: Cost analysis
Roll Cage Model A - Cost Analysis |  |  |  |  |  | 
Material | Weight (kg) | Cost/kg | Cost of Raw Material | Rate ($/hr) | Man Hours | Total Cost
AISI 1015 Steel (CDS) | 38.17433638 | $ 0.44 | $ 16.66 | $ 20 | 100 | $ 2,016.66
AISI 4130 Steel Annealed at 865 C | 38.07908198 | $ 0.51 | $ 19.61 | $ 20 | 100 | $ 2,019.61
6061-T6 | 13.09521259 | $ 2.20 | $ 28.82 | $ 30 | 100 | $ 3,028.82
2219-T87 | 13.77560119 | $ 2.17 | $ 29.89 | $ 30 | 100 | $ 3,029.89
7075-T6 | 13.63045162 | $ 2.30 | $ 31.40 | $ 30 | 100 | $ 3,031.40

## Slide 36: Decision Matrix
Material | Cost | Weight | Safety | Weldability | Machinability | Cost of Labor | Total | Weighted Total
AISI 1015 Steel (CDS) | 3 | 1 | 2 | 3 | 2 | 3 | 14 | 2.4
AISI 4130 Steel Annealed at 865C | 3 | 1 | 3 | 3 | 2 | 3 | 15 | 2.7
6061-T6 | 2 | 3 | 1 | 2 | 3 | 2 | 13 | 1.9
2219-T87 | 2 | 3 | 2 | 2 | 2 | 2 | 13 | 2.1
7075-T6 | 1 | 3 | 3 | 1 | 2 | 1 | 11 | 1.9
Weight | 0.1 | 0.1 | 0.3 | 0.2 | 0.1 | 0.2 | 1.0 | 
Material | Cost | Weight | Safety | Weldability | Machinability | Cost of Labor | Total | Weighted Total
AISI 1015 Steel (CDS) | 3 | 1 | 2 | 3 | 2 | 3 | 14 | 2.4
 | 3 | 1 | 3 | 3 | 2 | 3 | 15 | 2.7
6061-T6 | 2 | 3 | 1 | 2 | 3 | 2 | 13 | 1.9
2219-T87 | 2 | 3 | 2 | 2 | 2 | 2 | 13 | 2.1
7075-T6 | 1 | 3 | 3 | 1 | 2 | 1 | 11 | 1.9
Weight | 0.1 | 0.1 | 0.3 | 0.2 | 0.1 | 0.2 | 1.0 | 

## Slide 37: Energy Absorption – Front Collision
Objectives:
Crash Zone
Max Speed
Mass of Full Trike
Tools:
Impulse
Impact Force Equation
Newton’s Laws of Motion

## Slide 38: Stress Analysis – front collision
Outcomes at Crash zone of 0.6m
  Impact Force
  Energy Absorbed
  Deceleration felt by driver

## Slide 39: Stress Analysis – Complete Rollover
Weight is in the back of the trike
Driver is protected from rollover
Structure is further improved with:
  Larger diameter tubing
  Thinner wall

## Slide 40: Model B

## Slide 41: Design Approach
Maximize Comfort
Driver Protection
Improved Driver Controls
914mm driver cabin space
Damped front and rear suspension
Maximize ground clearance
Steering position and 3:1 turn ratio
Foot pedals
Visually appealing
603 mm energy absorption zone in case of frontal impact
Safe for travel at 45 mph, or 20 m/s

## Slide 42: Maximizing comfort-Cabin Space
In previous design the driver has approximately 27” of leg room before the front bar of the frame.
Rear swing arm linkage was approximately 21”
Driver’s legs would hang over the front bar of frame
Swing arm was this long because it carried the batteries
685 mm
533 mm
914 mm

## Slide 43: Cabin Space- Solution
Relocate the batteries to the sides of the original frame, using cages that will serve to strengthen the original frame, and can be used as a floorboard.
Decrease rear swing arm length since it no longer carries the batteries
Add in structure to both support the seat and can serve as a fender frame for the rear tire.
914 mm
381 mm

## Slide 44: Damped Front Suspension
Supported by offset members attached to battery cages
of travel
Spring/Damper setups are easy to source
Damper distance from wheel gives a firm ride
Firm ride is usually less comfortable but provides better suspension control.
552 mm
355 mm

## Slide 45
D
A
B
C
A
B
C
Distance from pivot to wheel center,
Extended Shock Length
Vertical height
D
Distance from pivot to wheel center,
Vertical height
Suspension Travel
Compressed Shock Length
Current
Suspension Travel with Damper Geometry
Static
Deflection

## Slide 46: Damped Rear Suspension
Currently the trike has one single damper mounted at the center.
This design uses two dampers to avoid torsion at the shock mounts.
Assumed suspension travel of
Dual dampers also provides more ride control and helps avoid sag when loaded.

## Slide 47: Rack And Pinion
The rotation of the pinion causes linear motion of the rack which turns the wheels left or right.
Can be found on cars, mini vans, and small suvs.

## Slide 48: Improved Driver Controls-Steering
Previous model had quick turn go-kart style steering.
At 45 mph, quick steering can pose a danger if the wheel is turned too quickly.
Rack and pinion steering allows more precise control of the vehicle’s steering.
Steering Ration 3:1

## Slide 49: Turning Radius Calculations
Parameters ​​ | 
Wheelbase(L)​​​ | 1.34 m​​
Track width(d)​​​ | 1.31 ​m​​
Inner Angle​(A)​ | 21.09°​
Outer Wheel​(B)​ | 16.55°​
Assume:
Turning Radius of 4 meters.
Actual Turning Radius
R= d/2+[L(cosec (A/2+B/2))]
R= 4.8 meters
1.34 m
1.31 m

## Slide 50: Comparison- Steering
​​ | Pitman arm Steering​​ | Rack and Pinion Steering​​
Complexity ​​ | ​less complex, easily machined​ | ​More complex due to a system of gears​
Durability ​​ | ​Contact with surfaces are less which leads to high durability​ | ​More wear takes place due to gear.​
Vibration ​​ | ​Vibration is less​ | ​More vibration in steering wheel​
Weight | ~5 lbs | ~7 lbs
Cost ​​ | ​30-70 $​ | ​50-150 $​
Common material used​​ | ​Alloy steel, Carbon steels, Iron​ | ​steel, aluminum ​

## Slide 51: Improved Driver controls-Foot pedals
In the previous design the control pedals would have to hang over the front bar of the frame.
With model B, the pedals can be mounted within the cabin.
Driver will be raised from the floor, allow feet to be in a more comfortable position.

## Slide 52: Roll cage For Model B
Objectives:
Safety
Easily accessible
Comfort
Aesthetics

## Slide 53: Roll Cage
Model B had 15cm removed from rear swing arm.
Use those extra 15cm to add crumple zone in front of trike.
Battery cages are attached to frame at the same level, then lateral supports between both cages add strength to the design in the event of a lateral impact.
Roll cage B adds support for rollover conditions uses the front 15cm provided by the shortening of the rear swing arm.

## Slide 54: Energy Absorption – Front Collision
Roll cage material ASI 1015
Dimensions of bars: 21.3 mm x 2.3 mm
Energy Absorption Area is 303mm x 441mm
Roll cage weights 48kg
Total Weight of Turbo trike 344kg
Force of impact during crash, with energy absorption zone
N
660 or = 67.28g’s
=6884 N*sec
D

## Slide 55: Front Collision with Bumper
Total Weight of Turbo trike m=344.2kg
D= 0.60m Force of impact during crash, with energy absorption zone
N
or = 33.94g’s
D

## Slide 56: Roll cage Benefits
Large surface area on top of the roll cage for solar panels
Easy to weld
Higher seat position which allows driver a better visibility
Comfort

## Slide 57: Components For Both Models

## Slide 58: Turbo Trike
1st Gen
Do not have any sensors incorpotated to the trike
Does not have any lights or turn signals
No solar panels
No regenerative braking
2nd Gen
Lidar sensor for auto braking with and adruino board
Front and back lights with turning signals
Solar panels
And regenerative braking

## Slide 59: Comparing Different Sensors

## Slide 60: TF03 Long-Distance LiDAR Module
Lidar sensor range from .1m to 180m
10khz frequency measure
100klux Anti strong light with IP67
Can easily communicate with the Arduino through UART
Anti-shock and anti-vibration can operate between –25-60 degrees Celsius
Cost $229

## Slide 61: Calculating Stopping Force
The program also calculate the speed and the amount of force needed to decelerate when an object is detected at a given distance
Depending on the distance and the acceleration of the trike the program will calculate how much force the regenerative braking needs to apply in order to prevent a collision

## Slide 62: Auto Braking

## Slide 63: Schematic

## Slide 64: Demostration

## Slide 65: Where do sensors Go?
Production vehicles use a wide range of sensors all throughout the car.
Of course, all the sensors responsible for auto braking are near the front with most being integrated into the front bumper

## Slide 66: Sensors on the Turbo Trike
First design involved the TF03 sensor under the top part of the roll cage.
Final design will have both lidar sensor at the front of the bumper
Will be capable of protecting the sensors from damage in minor collisions.

## Slide 67: Bumper Impact test (10mph)
Acceleration =
Force =

## Slide 68: Regenerative Braking
Tradition vehicles use friction to slow down and dissipates all the kinetic energy as heat
Regenerative braking allows the motor to turn mechanical energy to electric energy.

## Slide 69: Brushless DC Motors
The Turbo Trike is outfitted with a Kelly Controls brushless DC hub motor.
In each pair of stator teeth, the coils are activated independently to induce an electromagnetic field.
Permanent magnets on the rotor follow the electromagnetic field produce the torque the moves the vehicle.
When regenerative braking is activated the only on pair teeth will be active attempting to hold the permanent magnet in place slowing the vehicle.

## Slide 70: Regenerative braking
Efficiency
Effectiveness
  Depends on terrain, driving conditions, and vehicle size.
  Largest factor being vehicle size. Small personal ev’s see much smaller benefits, around 4-8%

## Slide 71: Parallel vs. Serial Regenerative Braking
Regenerative braking force and friction braking force increases together.
Does not require the use of an additional brake controller.
Effectiveness 9-18%
Adjustable braking system that uses a controller to vary amount of braking torque by friction Brakes and regenerative brakes.
Allow regenerative brakes to apply maximum braking force before friction brakes are applied
Requires brake by wire system.
Effectiveness 15-30%
Parallel
Serial

## Slide 72: Parallel Vs. Serial Regenerative Braking
Parallel Serial

## Slide 73: Parallel Vs. Serial Regenerative Braking
 | Complexity (0.5) | Effectiveness (0.3) | Pedal Feel (0.2) | Total
Parallel Braking System | 4 | 3 | May compromise pedal feel, but can be adjusted 3 | 3.5
Serial Braking System | 2 | 4 | Smooth and linear 4 | 3

## Slide 74: Implementation of Brakes
Throttle is on handlebar and individual hand brakes for the left and right wheel.
The pedals will be operated by the left and right foot similar to a go-kart.
Potentiometers will be attached to the axial at the pivot of the pedals and will be protected by small metal boxes.

## Slide 75: Implementation of Brakes
Tensile hook springs will be used underneath the plate to return the pedals to neutral position.
Original cable driven brakes will be kept to work in tandem with the regenerative brakes.
Tension and length of cable can be adjusted to reach appropriate pedal feel.

## Slide 76: Solar Panels History
Photovoltaic cells have been around since the late 1800s
Modern solar cell were created in 1954
More Americans are installing Solar Panels on their homes
As of 2020 the U.S has 97 gigawatts of Solar capacity
About 18 million homes can be powered solely from Solar Power
Becoming more efficient and more affordable

## Slide 77: Solar Panels on Vehicles
- Toyota
Created 0.03 mm thick Solar cells to put on the Prius.
- Tesla
Adding a solar option on the Cybertruck that can add 15 miles of range.
- Hyundai
Added a panel that can charge 30% to 60% of battery
Aptera
  Panels can charge up 40 miles of range a day
- Lightyear One
Has 5 of the roof and hood full of solar cells
that adds 40 miles of a range a day

## Slide 78: What are We Solar Charging ?
Current Setup ​
Two 36 V LiFePO4 Batteries powering a 3kW-48V Brushless Motor​​
Battery Specs​
Brand - BYD
Actual Voltage - 32.8V​
Number of Cells 10 in series​
Connected to the Battery in Parallel
Estimated Combined Battery Capacity ​
3600 watt-hours or 100 amp-hours​

## Slide 79: What is the Goal?
The goal is to not have to rely on the grid for charging
People on average drive 30 miles a day.
Current Estimated Battery Range
90 miles a charge
Energy usage per mile
Energy needed to drive the average
1200 𝑤h for 30 miles
The system needs to make at least 1200wh

## Slide 80: Decision Matrix for Solar Panels
Panel Arrangement | Voltage | Current | Wiring Simplicity | Total
Series | 5 | 4 | 5 | 13
Parallel | 0 | 5 | 1 | 6
Series
Parallel

## Slide 81: Decision Matrix for Solar Panel Type
Solar Panel Type | Price | Efficiency | Longevity | Options | Size | Total
Monocrystalline | 4 | 5 | 5 | 5 | 5 | 24
Polycrystalline | 5 | 3 | 5 | 0 | 4 | 17

## Slide 82: Decision Matrix for Panels
Solar Panel Type 100w | Average Price | Efficiency | Nominal Voltage | Bendability | Mass (kg) | Total
Renogy Rigid Panel (Mono) | 5 | 3 | 4 | 0 | 1 | 13
Renogy Flexible Panel (Mono) | 3 | 4 | 5 | 5 | 5 | 22
Number of Flexible Panels | Average Price | Nominal Voltage in Series (V) | Mass added trike (kg) | Area Needed | Total
2 | 5 | 1 | 5 | 5 | 11
3 | 4 | 5 | 4 | 4 | 13
4 | 2 | 4 | 2 | 2 | 8
5 | 1 | 3 | 1 | 1 | 5

## Slide 83: Solar System Schematic
Solar panels in series will give the system the needed voltage to charge the batteries.
Charge Controller needs to be rated for 36v system.
Fuse and charge disconnects gives user more control over system
This system can achieve 1200 W with 4 hours of sunlight at peak performance
300 watts * 4 hrs =1800 wh

## Slide 84: Possible Fitments on Trike
Model A
Model B

## Slide 85: Cost Comparison
Price of Panels
$169.99 x 3 = $509.97
Amount of Energy Created per Day
1800 Wh
Peak Energy Created in a Year
= 511 kWh
Savings from Using Panels
Energy Generated * Price of Energy = Money Saved
511 kWh * $0.22/kWh=$112.42
Amount of saved per Year
Using the Grid
Cost of Electricity
$0.22/kWh
Cost of Charging per Day
Cost in a Year

## Slide 86: Street Legal
In order to make turbo trike street legal:
Headlight
Taillights
Turn signals
Horn
Mirrors
Speedometer
Helmet

## Slide 87: Head Light System

## Slide 88: Turn Signal System

## Slide 89: Tail light System

## Slide 90: Final Steps
Converter – Battery 36V and designed system works at 12V
Seatbelt
Inspection
Title and Registration
Insurance
License plate

## Slide 91: Max lateral acceleration

## Slide 92: How many g’s can We Pull
Model A
HG = 0.42
LG = 0.56
WB = 1.5 m
TR = 1.3 m
Model B
HG = 0.60 m
LG = 0.57 m
WB = 1.3 m
TR = 1.3 m

## Slide 93: Outrigger Wheels
Our design will incorporate a set a wheels placed 0.523 m out from the rear wheel and only 0.036 m from the ground.
The design will allow for a max of 15° of lean before enough force is applied to push back.

## Slide 94: Spring design

## Slide 95: Spring Design
Hooke’s Law

## Slide 96: RC Models
RC Models 3D printed with PLA and PLA+
Uses off-the-shelf hobby components
Used to test suspension performance and vehicle dynamics
Model A
Model B

## Slide 97: Modified Frame
Model A
Model B

## Slide 98: Final Decision Matrix
 | Simplicity | Cost | Ergonomics | Length | Tip-Over
Weights | .2 | .1 | .1 | .05 | .15
Model A | 5 | 4 | 2 | 3 | 4
Model B | 2 | 2 | 5 | 4 | 2
 | Steering Ratio | Safety | Mass | Total | Weighted Total
Weights | .1 | .15 | .15 |  | 
Model A | 1 | 3 | 4 | 26 | 3.38
Model B | 5 | 4 | 3 | 27 | 3.09
Due to the weightings of each criteria, Trike A is the most viable option

## Slide 99: K-12 Requirement
Three wheeled vehicle
Four-wheel Vehicle
Solar Panel and Battery Equations
Energy (Wh) = Voltage (V) * Capacity (Ah)
Energy Density (Wh/g) = Voltage (V) * Specific Capacity
Discharge Time = Capacity (Ah) / Current (I)

## Slide 100: K-12 Requirement

## Slide 101: Questions?