## Slide 1: 8.2 Mini drone Senior Design Expo presentation
California State University, Los Angeles
College of Engineering, Computer Science and Technology​
8.2 Mini Drone
Alexander Magana
Robert Engler
Omar Jarquin
Tiffany Alvarez

## Slide 2: Agenda
Background .........................Tiffany & Alexander
Project Management .......................... Alexander
Technical Details ...............Tiffany, Robert & Omar
Assessment of Requirements .................... Tiffany
Summary ..................................... Alexander

## Slide 3: Agenda
Background .........................Alexander & Tiffany
  Background & Applications
  Model-Based Design
  Objective

## Slide 4: Background & Applications
Background:
MathWorks competition
Mini Drone Model: Parrot mambo Drone
Applications:
Package Delivery
Surveillance
Agriculture

## Slide 5: Model-Based Design
Model – based design uses a virtual representation or simulation to test a product before its final production
Drone hover simulation on Simulink vs reality

## Slide 6: Objective
Create a Simulink algorithm to autonomously command a drone to take off, follow a designated path and land in a marker while autocorrecting any deviations caused by obstructions.​
​
Design modifications to enable the drone to pick up a Rubik’s Cube from an assigned location and be able to return it without dropping it.

## Slide 7: Agenda
Background ............................... Andres Silva
Project Management ...........................Alexander
  Organization/Work Breakdown Structure
  Project timeline
  Design Process
  Deliverable

## Slide 8: Organization

## Slide 9: Project Timeline

## Slide 10: Deliverables
Deliverables | 
Completed | Not Completed
Full Simulation (Simulink) | Troubleshooting
3-D Printed Claw | Flying through Disturbances
1st Test Flight | Object Detection

## Slide 11: Agenda
Background ............................... Andres Silva
Project Management ................... Alexander Magana
Technical Details .....................Robert & Tiffany
  Simulink

## Slide 12: Image Processing
Left to right
First three blocks: Image post processing
Creates a matrix of 0s and 1s
Three submatrices: top left, top middle, top right
Used to determine position over path and landing initiation
Output sent to path planning

## Slide 13: Control system
Obtains sensor data from ultrasound, gyro and camera sensors.
Outputs are used to control how the drone responds to its environment.
The orange highlighted box is where the path planning is located.

## Slide 14: Path planning diagram
Designed to allow the drone to rotate and translate.
Utilizes data from ultrasound, gyro and camera sensors to conduct maneuvers.
Allows the drone to follow a set path.

## Slide 15: Chart 1 (rotation & translation)
Allows the drone to make maneuvers and decisions based on image processing, ultrasound and gyro sensor data.
Conditions are set for each state.
Dx and Dy represent small changes in the drone's position based on velocity and yaw.
Zout values are obtained through simulation and testing.
  Zout is read as a negative value because of the ultrasound sensor configuration.

## Slide 16: Chart 2 (Rotation)
Vision-based Data is the input.
Demonstrates conditions set for right and left turns.
Rate of rotation is controlled by the gain block “K”.
  K = 0.00456
    Obtained through simulation and testing.
Bottom portion of the Path Planning Diagram.

## Slide 17: Agenda
Background ............................... Andres Silva
Project Management ................... Alexander Magana
Technical Details .................................Omar
  Claw Design & Analysis
  Product Analysis

## Slide 18: Maximum Lift Capacity
Calculated max lift output of drone
95% of lift capacity used to determine allowable additional mass
Max allowable additional mass 68.5 grams
Power: Weight Ratio
  Hobby: 2:1
  Competition: 8:1

## Slide 19: Payload details
Payload | Mass (grams) | Dimensions (mm)
3x3 | 94.8 | 57 x 57 x 57
2x2 | 63.5 | 46 x 46 x 46
Mini 3x3 | 12.6 | 30 x 30 x 30

## Slide 20: Possible design configurations
Pros:
Symmetric design simplifies flight adjustments
Cons:
Requires relocation of belly mounted sensors
Would require longer motor power cable
Pros:
Doesn’t require sensor relocation
Could use OE motor and connector
Cons:
Non-symmetric WRT to center of mass

## Slide 21: Subframe design options
Subframe V1
4 rigid legs directly attached to subframe
Subframe V2
2 landing rails directly attached to subframe

## Slide 22: Fabrication limitations and design solutions
Issues:
Teeth too fine for 3D printer to render properly.
Not enough contact surface on grabber arm.
Solution:
Reduce # of teeth by half and expand contact pad by over 200% of original width
Issues:
Too thin of a wall caused failure when removing from 3D printer support material
Solution:
Double wall thickness and overall motor housing size
Issue:
With new gear teeth spacing, OE worm gear no longer meshed with arms.
Solution:
Create new worm gear with adjusted spacing for new teeth size

## Slide 23: Subframe v1 static analysis
Peak Stress
8.88e+5 N/m2
Peak deflection
.15mm
Calculated Factor of Safety
FoS of 34.7

## Slide 24: Subframe v2 Static Analysis
Peak Stress
1.803e+6 N/m2
Peak deflection
.057mm
Calculated Factor of Safety
FoS of 17.1

## Slide 25: Cost, Material, and Fos analysis
Design | Material | Total Weight (g) | Total Printing Time (hr:min) | Model Material Cost | Cost per Unit | Factor of Safety (FoS)
V1 | ABS | 27.11 | 6:50 | $3.87 | $13.65 | 34.7
V2 |  | 26.84 | 6:09 | $3.81 | $12.81 | 17.1

## Slide 26: Future Design improvements
Mk2.1 Improvements:
Added support to reduce bending under the applied load
New FoS of 70.6

## Slide 28: Flight Test Video

## Slide 29: Agenda
Background ............................... Andres Silva
Project Management ................... Alexander Magana
Technical Details ........ Omar Jarquin & Robert Engler
Assessment of Requirements .................... Tiffany
  Testing
  Risk Assessment

## Slide 30: Testing
Requirement | Source | Testing (1=Simulation, 2=Reality) | Verification
Hover | MathWorks | 1,2 | Hover in both testing phases at a fixed altitude
Line Follower | MathWorks | 1,2 | Complete several track with different lengths and angles
Landing | MathWorks | 1,2 | Land within the marker with >80% accuracy
Disturbances | Dr. Thorburn | 2 | Redirect onto the track when deviated
Claw Design | Dr. Thorburn | 1,2 | Stress and mass analysis
Augmented Flight | Dr. Thorburn | 2 | Pick up package and complete tracks
Time | MathWorks | 2 | Time log

## Slide 31: Risk Assessment
Requirement | Risk | Mitigation
Hover Algorithm | Simulated algorithm may behave differently in drone once ported. Causes include motor power, mass differences and battery voltages | Analyze drone behavior and calibrate algorithm as needed until desired outcome is reached.
Line Follower Algorithm | Algorithm may have trouble picking up the correct color for the path and landing marker once ported. | 
Land on Marker Algorithm | Impact may cause drone to flip or bounce out of the marker | Create a slow landing at marker
Flight with Augmentation | Printed parts may break at any point during testing or the competition | Spare parts where printed
Time | Should complete track efficiently and quickly | Algorithm was tested and calibrated as needed

## Slide 32: Risk Assessment
Plan A: Possible School Access
  3D print claw
  Test claw experimentally
  Deploy algorithm in coopetition
Plan B: Strictly Remote
  Claw design would not be 3D printed
  Testing of claw and algorithm would be done through simulation

## Slide 33: Agenda
Background ............................... Andres Silva
Project Management ................... Alexander Magana
Technical Details ........ Omar Jarquin & Robert Engler
Assessment of Requirements ............ Tiffany Alvarez
Summary ......................................Alexander

## Slide 34
Goals Accomplished in Spring 2021
Full Simulation on Simulink
Completed Claw Design
Test Run
Future Improvements
Improved Claw Design
Thrust Control (Simulink Code)
Summary

## Slide 35: Thank You