## Slide 1: Senior Design - Final Project April 25, 2021
Group Members: Lazaro Cano Hernandez
Brian Santiago
Nikolina Glamuzina
Peiwei Yu
Advisor: David Scholler
California State University, Los Angles
Engineering and Technology Department
Mini-Drone: Team 3

## Slide 2: Agenda
Background/Project Statement
Requirements
Project Overview
Software Development
Mechanism
Conclusion
Notes: The agenda for this presentation will be a quick overview of the project background and objectives, its requirements, discussion of the software developed for simulation and the pickup payload mechanism, as well as as short videos of the simulation model and drone trial.

## Slide 3: Background
What is a UAV
An unmanned aerial vehicle operated under remote control of a human or autonomously (i.e., without human intervention)
UAVs are used worldwide and have the capability to perform specific missions autonomously
  Used for aerial photography, delivery, combat, surveillance, etc.
Parrot Mambo Fly
UAV interested in: Mini-Drone
4 Available Sensors: Ultrasound, Pressure, IMU, Camera
Notes: Drones are used more frequently in recent years and will continue to become more and more useful in the future. With the ability to be controlled remotely or autonomously, they have a multitude of industries such as combat, surveillance, and aerial photography. Even complex machines as these can be modeled and coded to tackle many problems.
The project focuses on the design of drone software on Matlab SIMULINK for it to autonomously identify and follow a path. The drone in question is a Parrot Mambo Fly and has four available sensors used to aid it in flight: the ultrasound and pressure sensor, both used for altitude estimation, the IMU, which relays data about rotational and angular speed, and the camera sensor, which give visual data of the space directly below the drone.

## Slide 4: Project Statement
To modify a commercial drone to autonomously identify and fly a path.
  Develop a Simulation code to run on Simulink software for an autonomous flight
  To develop the software onto hardware for drone to follow intended path
Develop an attachment mechanism
  To develop an attachment payload pickup mechanism for the drone to pick up a payload and return to starting position
This project is multipurposed:
Notes: The object of this project can be explained in two points. The first desire was to modify a commercial drone to autonomously identify and fly a path, which includes developing a simulation code on Simulink and implementing that software onto the hardware of the Parrot Minidrone. The second is to development an attachment mechanism, wherein the drone will fly a path, retrieve a payload, and return to its starting position.

## Slide 5: Requirements
Functional Drone Requirements:
  Start drone autonomously from starting position
  Drone lifts to designated altitude
  Orientates itself
  Identifies path
  Track the path
  Stabilize and correct from environmental disturbances
  Lands on landing pad
  Drone turn off
Mechanism Requirements
Pick up Rubik's cube (3x3x3 cm, 25 grams) with least amount of time
Not interfere with drone's flight capability/sensors
Maintain weight distribution and stability
Notes: Within this project, there were set requirements the drone had to accomplish in its simulation, from identifying the path, autonomously following the path and remaining within its boundaries, correcting itself when coming across an environmental disturbance, and landing on the landing pad at the end of the path.
Concerning pickup mechanism, its requirements are simple. It must be able to pick up a Ribuk’s cube of 3-by-3-by-3 centimeters, approximately 25 grams. As the drone picks up the cube, it must maintain its weight distribution, thus keeping its center of mass the same and remain stable as it flies.

## Slide 6: Project Overview
Simulink Modeling
  Autonomous Path
  Optical Flow & State Flow
Imbedding Code onto Drone Hardware
  Drone Trials
Mechanism
  Design
  Manufacturing
  Drone Trials
Competition
  Simulation
  Path Identification
  Payload pick up
Notes: Within the project, the Simulink modeling took priority, with two major focuses: creating the drone to be autonomous with the use of stateflow and using optical flow alongside the camera sensor. Once the code was done, it was time for testing on the drone hardware. For the pickup payload mechanism, it was designed, modeled on SOLIDWORKS, manufactured, and tested. The competitions at the end of the school year are to show how the team faired with the project, testing how well their simulation runs, as well as how well the drone kept to the path on an actual run, and finally how well it can pickup the payload.

## Slide 7: Project Schedule
Notes: Here is a work breakdown structure and schedule of the the team’s work throughout the school year. It’s been broken into four phases: 1) the Simulink model, developing and implementing the code into the hardware, the mechanism, and participation in final competitions and presentations.
Most of the simulation progress was done during winter break to the spring semester, whereas the mechanism progress was mainly finished during the fall semester. The spring semester was used to test the drone simulation and drone hardware simultaneously, and fix problems as they came.
The team has had several milestones within the school year, four of which are within he spring semester. Because of the work done in fall, the mechanism was fabricated and attached to the drone. The team successfully completed the practice competition, which gave an insight on what needed to be worked on in order to prepare for the final competition.

## Slide 8: Software Development
( IMU, Pressure, Ultra-Sonic)
( Updated Reference Cmd, CH12,S4)
Notes: This control system block controls the rotational speed of the motors of the drone. Three main inputs are fed into this system: the AC command inputs, the reference commands, sensor data such as position and velocity, and image data from the camera. The sensor input exclude the camera sensor, which is its own input into the image processing subsystem.

## Slide 9: Software Development: Image Processing Overview
Opt flow
Video viewer
Color
B & W
Notes: This is an overview of the image processing subsystem within the flight control system and is key in aiding the drone to following its flight path. There are three basic functions to this subsystem: identifying the color of the path of the drone and path edge discrimination, highlighted in the red box, and to use optical flow to determine the x and y velocities of the movement between consecutive images, highlighted in the blue box. Within the red section, two video viewers are used, one to show the video feed of the camera sensor and the other focusing on the outputs of the edge detection block. The inputs are the image data from the camera sensor and the outputs are vision data of intensity values and horizontal and vertical velocity vectors.

## Slide 10: Image Processing (Color, B & W)
Notes: The main function of this subsystem is to identify the color of the path of the drone, this slide focusing on outlining the image processing steps. The input is the camera data that passes through a conversion block, returning RGB data, which then checks for the dominant color, simple chosen to be red. Logic blocks are then used to binarize the image- meaning if the values returns a value greater than the threshold, it returns a 1, if not , then it returns a 0). The binarized data is then summarized and passed through another threshold, which is then outputted to the control system.
Extra blocks are used to aid in edge discrimination on the path, comparing intensity values at the edge detected, to later aid the drone from overshooting the edges. Both visual data outputs are used for the drone to detect and follow the path in the control subsystem, colored and black and white.
(Make inputs/outputs blocks bigger)

## Slide 11: Optical Flow (Color Image) - Drone Velocity Vectors
Inputs:
Image 1
Image 2
M = number of corners detected
X position of corner detected
Y position of corner detected
Outputs:
Horizontal velocity
Vertical velocity
Using Lucas-Kanade Method
Obtains solution for Optical Flow using least squares (2x2 system)
Notes: The third function to this subsystem is to use optical flow to determine the vertical and horizontal velocity vectors, located in the blue box.
The inputs into this section of the code are the camera images and position values from a corner detection block, the outputs the velocity components.
Optical Flow is the distribution of apparent motion of brightness patterns within an image, the motion of the image pixels compared to neighboring pixels, and the Lucas-Kanade Method solves for these apparent velocities by using least squares. The MATLAB function block in the orange is the script that incorporates the Lucas-Kanade method. Errors using optical flow occur with low contrast and poor resolution of the images, and large motions captured between consecutive frames. With the increasing error proportional to the frame rate, the time between consecutive images must be small to get feasible velocities. The corner detection values help the drone focus on the edges of the path during turns.

## Slide 12: Control System Overview
B&W Intensities
IMU Dynamic Data
State Flow
Updated Reference cmds
Notes: (Divide into sentections, short time spent on this slide)
Reference commands for reference position
SIngle input signal from sensors, but within are signals representing position values, velocities, and yaw values, etc. The sensors are IMU, camera, pressure, and ultrasound.
Takes visual data from the image processing subystem, the intensity values into the state flow block to determine and identify the path.

## Slide 13
Intensities
MATLAB function displays intensities values of the drone’s camera
Used to make sure the Drone is within the path (red path has an intensity value of 1)
X-axis & Y-axis display the intensities values from a 3D axis.
These values are used to map out the path in real time
Section 1: B&W Intensities

## Slide 14
Subsystem Block
  Inputs
    Yaw
    Initial body rates (p, q ,r)
  Body rates (p q r) goes into a MATLAB function
    Integrating positions to evaluate the r value (Drone up position)
  New yaw value is determined
  Output
    Corrected Yaw
    Use to make drone rotate are any angle
    Input to State Flow block
      Autonomous Drone Path Identification (ADPI)
Section 2: IMU Dynamic Data

## Slide 15: Section3 : State Flow
State Flow (ADPI)
  Autonomous Drone Path Identification
Inputs
  x & y –axis position
  dx & dy
  Yaw
  Vision-based Data (redDetect)
Outputs
  YawOut
  xOut
  yOut
  zOut
Notes: (Divide into sentections, short time spent on this slide)
Reference commands for reference position
SIngle input signal from sensors, but within are signals representing position values, velocities, and yaw values, etc. The sensors are IMU, camera, pressure, and ultrasound.
Takes visual data from the image processing subystem, the intensity values into the state flow block to determine and identify the path.

## Slide 16: Section 3: State flow
Hovering/ Forward
Identifying Turns
Landing
Notes: Reference commands for reference position
SIngle input signal from sensors, but within are signals representing position values, velocities, and yaw values, etc. The sensors are IMU, camera, pressure, and ultrasound.
Takes visual data from the image processing subystem, the intensity values into the state flow block to determine and identify the path.

## Slide 17
Section 3.1: Hovering/Forward
When running the code:
Drone is command to hover at 0.9144 meters (equivalent to 3 feet) off the ground.
Hover for 4 seconds to give the done enough time to orientate itself.
Drone shall move forward when a red path is detected.
Drone come to a complete stop when the red path is no longer detected.

## Slide 18: Drone Trial: Wind Detect Video

## Slide 19
Section 3.2: Identifying turns
The drone shall turn desired orientation:
  (CW) when red is detected on the right side.
  (CCW) when red is detected on the left side.
Drone shall continue to move forward once its proper turn is complete.

## Slide 20
Section 3.3: Landing
Landing code
Once the end of the path is detected, the drone comes to a stop followed by a landing code.
Landing code helps the drone land on the red circle pad.

## Slide 21
Section 4: Updated Reference cmds
(0,0,0)
Reference Commands
(xOut,yOut,zOut)
Updated Reference Commands
Notes: This slide will talk about section four of the code, the reference commands. When the drone turns on, it has a set of reference commands. Its position is its origin and it doesn’t experience any yaw, not moving until those reference commands are changed. The outputs of the stateflow block are combined into one signal, the updated reference commands, which replaces its original reference commands, which is then fed to the drone motors. With each new change in state of the drone, the reference commands will be updated and the drone motors reaction to those updates.

## Slide 22: Software Development: Video

## Slide 23: Mechanism Concepts before designing
The drone can lift maximum of 38 grams
The payload is 25 grams
Maximum mechanism weight: 13 grams
Center of gravity
Center of gravity
Ultrasonic Sensor
Camera Sensor

## Slide 24: Mechanism Design
Pros:
Easy to attach
Weights 7.86g
Center of mass remains at the center
Cons:
Required 3D printing
Required replaceable 3M-Tape
Blocks the sensors after picking up the payload
Required waypoint follower when carrying the payload

## Slide 25: Trade studies
Not to block the ultrasonic and camera sensors until the cube has been picked up
Don't have to do additional modifications on the frame
No codes are required to control the mechanism
The mechanism will stick the cube as the drone lands

## Slide 26: Mechanism: Video

## Slide 27: Conclusion
WBS was defined for this Spring Semester
Competition requirements were met
Software development was completed
Mechanism model was manufactured and attached
Ready to be deployed