## Slide 1
ADVISOR: Michael Thorburn
Team Members:
Miguel Gopar
Lester Arauz
Gina Yama
Luis Lopez
Mini-Drone Final Design Presentation Team: Golden Eye Eagles Date:5/02/2021

## Slide 2: Agenda
Background, Objectives, and Requirements Luis
Work Breakdown Structure All
CAD Transferring and Findings Luis
The Grabber Gina
Image Processing Lester
State Flow Lester
Manual control Lester
Hardware tuning Miguel
Simulation Vs Real Life video Miguel

## Slide 3: Background
MathWorks is a company that specializes in computer language for technical computation.
The MATLAB program is used for data analysis, visualization, programming, computation and much more.
The MathWorks student competition was created to enhance creativity, teamwork and multiple possibilities for industry experience

## Slide 4: Objective
We were tasked to be able to modify a drone to be able to follow a designated path and detect an object.

## Slide 5: REQUIREMENTS
Requirements table​ |  | 
 | MathWorks Competition ​ | Senior Design​
 | Be able to detect the red guided path on the ground​ | Be able to detect the red guided path on the ground​
 | Be able to safely fly through a path​ | Be able to safely fly through a path​
 | Be able to with stand disturbances like wind ​ | Be able to with stand disturbances like wind ​
 | At the end of the path be able to land on a landing pad​ | At the end of the path be able to hover down and pick up a Rubik's cube​
 | ​ | Be able to hover back up and fly safely back to the beginning ​

## Slide 7: CAD Transferring Research
Import as a child or a ROOT component
XML files work better for Simscape
STL files work better for the (3D world editor) virtual simulation

## Slide 8: CAD Transfer #1
The SolidWorks Rubik’s model imported as a default part
But it can still be edited

## Slide 9: CAD Transfer #2
It simulates the model that the parrot Drone comes with
But we wanted our own model, So this was just for practice

## Slide 10: Findings for CAD Transferring for Simulation
I imported the grabber into world editor
Cannot simulate grabbing movement in the virtual world
We were advised to use Simscape
We switched from autonomously to manually

## Slide 11: Mechanical Grabber Mechanism
Grabber must follow ASME Standards
List of requirements some included
Must be able to pick up a 13.6g Rubic Cube.
Be able to open and close
Must not interfere with any components like camera, sensors
A Table of concept Decision matrix

## Slide 12: Grabber Parts List
List consist of
Part number
File name
Material applied
Manufacturing
Final check

## Slide 13: Grabber design
Part#: Drone-01—x3
Assembly1A
Part: Drone-02—x2
Assembly1b

## Slide 14: Grabber FEA and Safety Factor
Yield Strength for Part
Material starts to deform in a
Plastic like fashion
Results for ABS Material
Load of cube= 13.6 g/ 2.2e-3
Yield strength= 4.7e+07
Fails at Yellow color
Passes Test

## Slide 15: FEA and Factor and Safety Distribution
Material | Factor and Safety distribution
ABS Plastic | Min = 77.003
 | Max= 1000

## Slide 16: CAD: The Drone
Used the CADD from mini-parrot drone completion.
Drone was scaled down, no parts details
Droned was scaled up to meet with approximated Grabber dimensions
No solution yet

## Slide 17: Image Processing
There are 2 different methods that we are applying to the image processing.
  Hough transform
  Counting the number of pixels in an area.
Both methods require image thresholding.
Notes: Hough transform was used mostly to help find the line angles from the track and help generate the ability for the drone to know how to move forward
And pixel counting at the end of the track that helps to find the landing pad to land the drone within the circle

## Slide 18: Image Processing
Notes: So as you can see the bottom a home made track to simulate the matlab competition track due to covid lab
This is what the drone sees once it is hovering over the with the help of image threshold we were able to isolate all the colors that we did not need, and configured the drone to see on the red colors which helps the drone see the track

## Slide 19: State Flow
1. Start: sets initial position.
2. Path following: Based on image data.
3. Landing: Enables landing and searches for landing pad.
4. Pick up: (Untested) Locates object autonomously.

## Slide 20: Landing
Split drone image
Use pixel count to determine location
Land if more than 150 pixels in center

## Slide 21: Manual Control
Can control drone movement and claw opening.
Mapped keyboard keys to
different maneuvers

## Slide 22: Controls Tuning
The system has 4 separate controllers:
Yaw – PD; XY-to-Reference – PD; Attitude – PID; and Total Thrust – PID
Attitude and XY-to-Reference
Notes: Mostly to corollate for stability of the flying the drone and not letting is shake or vibrate when hovering
The following table is PID table helped us when using the attitude and xy PIDs guide what is happening in the P Porportional integral and derivative

## Slide 23: Hovering (Attitude Controller)
Rating | P_pr | I_pr | D_pr
Works with issues | 0.0013, 0.011 | 0.01 | 0.002, 0.003
Minor issues | 0.0015, 0.0015 | 0.015 | 0.001,0.001
Best | 0.014, 0.014 | 0.014 | 0.0022, 0.0022
•Trial and error to adjust drone response.
•Adjustments throw the drone into a roll or pitch.
•Around 10% difference in values.
Notes: The following values were a way of helping make the drone fly in real world conditions, in simulation the pid values were perfectly fine while when we connected the drone we had difficulty making the drone do the exact thing in simulation
In simulation the attitude controller values flew the drone with little to no errors, however when testing in real world conditions the drone would yaw, pitch, and roll into the wall.

## Slide 24: XY-to-Reference-Orientation
Controls adjustments to X and Y positions.
Converts to pitch and roll commands

## Slide 25: Adjustments For Claw
Claw will add additional weight to rear.
Will have to retune Controllers
Adjust power distribution of motors

## Slide 26: Simulation Vs. Real Lifetime Video
Successfully
completed all
simulations

## Slide 27: Drone Following Path
Notes: Please disregard the background this was the closest we were able to get a laboratory for testing due to covid
This is one of hundreds of test that did not crash into my wall
This had the hovering block connected to aligning block and that was connected to identifying the track and following forward

## Slide 28: Drone Aligning Itself
Notes: This was testing the drone to see the track on the bottom and once finding the line angles it was able to center itself to the track

## Slide 29: Questions
Questions will be answered after the execute summary presentation